Two Picture Template  ( note: pict size 3.8)

# Text boxes

Oil Filter (AC PF64) is hard to spot unless you know where it is and have a bright light. I used a ½” ratchet and extension bar to turn a cup-type filter wrench while my plastic drain tub was below the filter. Go slow. Oil will spray on the cross-bar as it does when removing the oil drain plug.

15mm Oil Drain Plug looking from driver’s side of CTS. I drained the oil pan first, as shown in pic below, then emptied the plastic drain tub into my transport bucket for reclaiming. Lastly, I filled the new AC PF64 Oil Filter with fresh synthetic 5W30 oil, smeared some oil on the new filter O-Ring and replaced the AC PF64 Oil Filter so that I could add 5 quarts fresh synthetic oil to the engine.

.

Jack Stand (Just in Case)

Rhino-Ramp

15mm Oil Drain Plug located on passenger side. Plug has an integral rubber washer. I used a 15mm combination wrench to get it loose enough to drain hot oil into my pan. It leaks onto the cross bar directly below it, so I just cracked it open and gave it 10 minutes, and I didn’t spill any on my driveway. After all oil is drained, wipe the oil from the pan and cross-bar, install cleaned drain plug by hand to prevent cross-threading, and tighten the drain plug firmly with the combination wrench. If I knew the proper torque setting, I would use my torque wrench on this drain plug.